## Slide 1: Neural Rendering of Multichannel BRIRs for Personal Sound Zones with Head Tracking
Tanay Mannikar, Yue Qiao

## Slide 2: Motivation
Compressed BRIR (binaural room impulse response) representation
Interpolation/extrapolation of unknown BRIRs
Real-time BRIR generation for PSZs with head tracking

## Slide 3
Analysis
Synthesis
(r, θ, φ)
(r, θ, φ)
Notes: 1. dataset analysis
    brtf fluctuations, motivation for regression model
    regression model – prove that scattering coefficients can perform in regression
    Future step: test for sparsity
2. synthesis model
    GAN/VAE with coefficients predefined layer during training

## Slide 4: Understanding BRIR Dependencies
Single-speaker BRIR measurements from dummy head
0:1:360°, rotation
0:1:90 cm, horizontal translation (L→R)
Bandpass filtering (150 Hz – 7 kHz)

## Slide 5: BRIR Spatial Dependencies
BRTF (Binaural room transfer function) = Fourier transform of BRIR
Fractional-octave smoothing applied to calculated BRTFs (1/6th octave)
Translational BRTF spectral power difference defined as:
Azimuthal BRTF spectral power difference defined as:
= BRTF vector
= log constant

## Slide 6
Spectral Power Difference vs. Azimuth
Smoothly shifting pattern over the translational range: easier to learn
Complex patterns: harder to learn
Head-related effects dominant

## Slide 7
Spectral Power Difference vs. Translation
Few distinguishable patterns over the azimuthal range: easier to learn
Multivalued pattern evolution: harder to learn
Room effects dominant

## Slide 8: Feature Extraction
Can BRIR frequency patterns be captured via feature extraction to match BRIRs to corresponding head orientations?

## Slide 9: Continuous Wavelet Transform (CWT)
[1] http://web.stanford.edu/class/ee269/LectureWaveletsPartII.pdf
Multiresolution signal analysis, unlike Short-Time Fourier Transform (STFT)
Motivation: improved analysis of quick impulses with high frequency information [1]

## Slide 10: Wavelet Scattering Transform
[2] J. Andén and S. Mallat, Deep scattering spectrum, IEEE Transactions on Signal Processing, vol.62, pp.4114-4128, 2014.
Extracts higher-order features from signals
Robust against deformations in time series and images [2]
Originally intended for dealing with sparse datasets
Notes: Powerful tool for image texture classification, speaker/phrase identification with very sparse datasets, timbre classification, etc.
Overcomes loss of high-frequency information in other commonly-used feature extraction methods such as MFCCs

## Slide 11: Wavelet Scattering Transform
input signal, e.g. time series, image
wavelet
lowpass filter
[3] W. Ghezaeil, L. Brun and O. Lézoray, "Wavelet Scattering Transform and CNN for Closed Set Speaker Identification," 2020 IEEE 22nd International Workshop on Multimedia Signal Processing (MMSP), Tampere, Finland, 2020, pp. 1-6, doi: 10.1109/MMSP48831.2020.9287061.
Notes: Extracts higher-order analysis features from signals for classification tasks [1]
Robust against deformations in time/spatial domain
Overcomes Fourier transform instabilities
Originally intended for classification with sparse datasets
Powerful tool for image texture classification, speaker/phrase identification with very sparse datasets, timbre classification, etc.
Overcomes loss of high-frequency information in other commonly-used feature extraction methods such as MFCCs

## Slide 12: Wavelet Scattering Transform
Scattering scale : ϕ(t) is of length samples
Notes: Mother wavelet for each order: morlet
Quality factor Q = 8, defines filterbank resolution

## Slide 13
[4] Kymatio: Wavelet scattering in Python - v0.3.0 “Erdre,” Classification of spoken digit recordings. https://www.kymat.io/gallery_1d/plot_classif_torch.html
Notes: Provides time-frequency representation of signal by convolving wavelets of varying time dilation across the signal to show similarity at each frequency bin – essentially a multiresolution filter bank
Differs from STFT in choice of time-frequency tiling for 1D signals : higher frequencies receive better time localization and over a wider range of frequencies, lower frequencies receive better frequency resolution over a wider range of time

## Slide 14
Notes: Provides time-frequency representation of signal by convolving wavelets of varying time dilation across the signal to show similarity at each frequency bin – essentially a multiresolution filter bank
Differs from STFT in choice of time-frequency tiling for 1D signals : higher frequencies receive better time localization and over a wider range of frequencies, lower frequencies receive better frequency resolution over a wider range of time

## Slide 15
Notes: Provides time-frequency representation of signal by convolving wavelets of varying time dilation across the signal to show similarity at each frequency bin – essentially a multiresolution filter bank
Differs from STFT in choice of time-frequency tiling for 1D signals : higher frequencies receive better time localization and over a wider range of frequencies, lower frequencies receive better frequency resolution over a wider range of time

## Slide 16
Apply log() to all scattering coefficients
Average (flatten) coefficients along time window index
Time-invariant representation!

## Slide 17: Model Comparison
[5] Massicotte, Philippe Yvan. Machine Learning with Feature Extractions for Regression Estimation of Binaural Sound Source Localization. doi: 10.22215/etd/2022-15283.
1D Convolutional Neural Network (1D-CNN)
Baseline model: BRIR-CNN
    Learns over raw time-domain information
Three candidate models: SCAT-CNN (J = 5, 6, 7)
    Learns over time-averaged log scattering coefficients [5]
Input: concatenated L/R ear BRIRs
Output: Head coordinates
{x, sin(), cos()}
Notes: Prior attempts have combined deep wavelet scattering networks with convolutional neural networks (CNNs) to perform binaural HRTF classification/regression [2] and robust speaker identification systems [3] on limited datasets with significant prediction accuracy
From [2], concludes that regression CNN allows for possible finer resolution predictions in HRTF azimuth and elevation/position predictions compared to standard classification approach
Model architecture for both CNNs builds off model in both [2] and [3] due to similarity of task

## Slide 18: Model Tradeoffs
SCAT-CNN
More compact/compressed = RAM-friendly
For smaller J values,
compression increases
BRIR-CNN
Higher model complexity = RAM-intensive
No compression (baseline);
learns over full time-domain signal
Notes: Prior attempts have combined deep wavelet scattering networks with convolutional neural networks (CNNs) to perform binaural HRTF classification/regression [2] and robust speaker identification systems [3] on limited datasets with significant prediction accuracy
From [2], concludes that regression CNN allows for possible finer resolution predictions in HRTF azimuth and elevation/position predictions compared to standard classification approach
Model architecture for both CNNs builds off model in both [2] and [3] due to similarity of task

## Slide 19: Training and Evaluation
Total dataset size: 32760 BRIRs (360 x 91)
Validation/training data split: 25/75 %
Loss metric: Mean Squared Error (MSE)
Evaluation error metric: absolute scaled difference between true and predicted translation/azimuth

## Slide 20
Notes: SCAT-CNN and BRIR-CNN perform similarly at time invariance of J = 7 (i.e. more time-domain averaging and spreading)
SCAT-CNN of J = 5 and J = 6 do not have enough resolution to capture finer differences in frequency shifts between BRIRs; prediction accuracy diminishes

## Slide 21: Takeaways
For x prediction, SCAT-CNN, J = 7 performs best
For φ prediction, J value is irrelevant

## Slide 22: Future Analysis Steps
Train both models with sparser datasets
Bandpass BRIRs to further limited frequency range(s) to reduce input size
Verify robustness against varying initial propagation delay

## Slide 23: Proposed Synthesis Work

## Slide 24
Analysis
Synthesis
(r, θ, φ)
(r, θ, φ)
Notes: 1. dataset analysis
    brtf fluctuations, motivation for regression model
    regression model – prove that scattering coefficients can perform in regression
    Future step: test for sparsity
2. synthesis model
    GAN/VAE with coefficients predefined layer during training

## Slide 25: Synthesis Approach
Transfer learning: pre-trained model weights
Fourier encoding ↔ phase information
γ(p) = {sin(2nπp), cos(2nπp)}, n = 0, 1, · · · , N
p = (r, Φ)
Time-averaged scattering coefficients ↔ frequency magnitude information

## Slide 26: Synthesis Workflow
(r, θ, φ)
(sparse dataset)
(r, θ, φ)
Neural Network 1
Wavelet
Scattering
Transform
Coefficients
Neural Network 2
1
2
3
(full dataset)
Frequency magnitude-dependent
learning
Phase-dependent learning

## Slide 27: Conclusions
Scattering coefficients
    Allow compact BRIR representation
    Efficiently represent room-related effects (x)
    Poorly distinguish head-related effects (φ)

## Slide 28
[1] http://web.stanford.edu/class/ee269/LectureWaveletsPartII.pdf
[2] J. Andén and S. Mallat, “Deep scattering spectrum,” IEEE Transactions on Signal Processing, vol.62, pp. 4114-4128, 2014.
[3] W. Ghezaeil, L. Brun and O. Lézoray, "Wavelet Scattering Transform and CNN for Closed Set Speaker Identification," 2020 IEEE 22nd International Workshop on Multimedia Signal Processing (MMSP), Tampere, Finland, 2020, pp. 1-6, doi: 10.1109/MMSP48831.2020.9287061.
[4] Kymatio: Wavelet scattering in Python - v0.3.0 “Erdre,” Classification of spoken digit recordings. https://www.kymat.io/gallery_1d/plot_classif_torch.html
[5] Massicotte, Philippe Yvan. “Machine Learning with Feature Extractions for Regression Estimation of Binaural Sound Source Localization,” doi: 10.22215/etd/2022-15283.